## Slide 1: Single Crystal Software Workshop ECM21-2003
Louis J. Farrugia,
Department of Chemistry
University of Glasgow
GLASGOW G12 8QQ
Scotland
Processing of Bruker & Nonius CCD data

## Slide 2: Single Crystal Software Workshop ECM21-2003
Processing of Bruker & Nonius CCD data
There are two main stages of CCD data processing :
First procedure is specialised, involves many corrections to the raw CCD data - no facilities in WinGX for this (Denzo, EvalCCD, SAINT).
Second procedure is handled in WinGX by a variety of routes
Frame integration relies on “black box” commercial software.
Frame integration - extraction of intensities from images
Post processing - error modelling, merging, abs corrections, etc

## Slide 3: Single Crystal Software Workshop ECM21-2003

## Slide 4: Single Crystal Software Workshop ECM21-2003
Denzox program
Denzox was written by Bob Blessing, but extensively modified in Glasgow
Reads .x files produced by Denzo and concatenates data
does little massaging of reflection intensities
transfers fulls transparently - no change in I or (I)
simple statistical summation of partials to provide I and (I)
some rejection criteria - 2 of fit, partials at edge of scan set, sin/
calculates direction cosines
re-indexing for equivalent orientation matrices (NOT re-orientation !)
various possibilities for batch number - frame, scan-set, experiment
output file denzox_hkl.sortav for Sortav (or Gaussian abs correction)
output file denzox.sad for Sadabs

## Slide 5: Single Crystal Software Workshop ECM21-2003

## Slide 6: Single Crystal Software Workshop ECM21-2003
Processing of KappaCCD data

## Slide 7: Single Crystal Software Workshop ECM21-2003
Processing of KappaCCD data
Most data reduction programs handled through KappaCCD GUI
Load cell from various sources
Filter data by sin() or batch no.
Quick view of data quality by Weiss or Diederich - Karplus programs
Concatenation of input files
Plots (Sortav)

## Slide 8: Single Crystal Software Workshop ECM21-2003
Processing of KappaCCD data
Most data reduction programs handled through KappaCCD GUI
Load cell from various sources
Filter data by sin() or batch no.
Quick view of data quality by Weiss or Diederich - Karplus programs
Concatenation of input files
Plots (Sortav)

## Slide 9: Single Crystal Software Workshop ECM21-2003
Denzox GUI
Denzox by R. Blessing
Reads .x files and
calculates direction cosines + batch no.’s
Writes out files
denzox_hkl.sortav
denzox.sad
Reads .x files from disk files or CD-ROM
Allows for Denzo matrix variation

## Slide 10: Single Crystal Software Workshop ECM21-2003
Sortav GUI
Sortav by R. Blessing
Pre-correction with GAUSSIAN abs. cor.
Apply frame/batch scaling
Apply empirical absorption correction
Data merging & reject outliers
Check that parameters are correct !

## Slide 11: Single Crystal Software Workshop ECM21-2003
Sortav GUI - Empirical absorption
Requires sufficient data redundancy
Uses spherical harmonics to model absorption anisotropy
Odd harmonics used to model non-centrosymmetric systematic errors
-dependency also possible
R. H. Blessing, Acta Crystallogr., Sect A 1995, 51, 33-38.

## Slide 12: Single Crystal Software Workshop ECM21-2003
Sortav GUI - Merging
Several schemes for outlier rejection
Normally use Tukey downweighting and rejection of outliers
“Autoreject Outliers”
until no further ones found
R. H. Blessing, J Apply Cryst 1997, 30, 421-426

## Slide 13: Single Crystal Software Workshop ECM21-2003
Sortav GUI - Output
Save intermediate results here
Controls number of plots and verbosity of output.
Remove unwanted files
R. H. Blessing, J Apply Cryst 1997, 30, 421-426

## Slide 14: Single Crystal Software Workshop ECM21-2003
Sortav GUI - Results
Shows outliers and rejected reflections
Shown missing reflections
R. H. Blessing, J Apply Cryst 1997, 30, 421-426

## Slide 15: Single Crystal Software Workshop ECM21-2003
Processing of SMART/SAINT data
Reads in all .RAW files
found in directory
Provides ranges of Intensities, exposure time, frame numbers.
Necessary to provide batch numbers for scaling.
In this example, files should be processed in four batches

## Slide 16: Single Crystal Software Workshop ECM21-2003
Processing of SMART/SAINT data
Choose which sets of RAW
files to concatenate

## Slide 17: Single Crystal Software Workshop ECM21-2003
Processing of SMART/SAINT data
Choose which sets of RAW
files to concatenate
Decide on way to derive batch numbers for scaling
Write file concat_hkl.sortav
which is exact translation of the data in RAW file.
Suitable for merging etc with Sortav